CITY	OF EVART

FIRE DEPARTMENT

HAZARDOUS MATERIALS REPORTING HANDBOOK

THIS PAGE INTENTIONALLY LEFT BLANK

START YOUR REPORTING PROCESS BY READING THIS PAGE FIRST.  It will help you file properly.  If you have questions about how to fill out the HMIS Document, please call the Evart Area Fire Prevention Division at 231 734 5521.

1.  REVIEW HMIS REPORTING GUIDEBOOK: It contains definitions and reportable amounts that you’ll need to complete the HMIS form.

2.  COMPILE YOUR MSDS DOCUMENTATION: The Material Safety Data Sheet (MSDS) will provide you with most of the information you need for this reporting procedure.  DO NOT SEND MSDS’s to the fire department unless specifically requested by the fire department. Information not contained on the MSDS can be obtained from the manufacturer.

3.  SEPARATE YOUR MSDS DOCUMENTS into categories listed on the Reportable Amounts Table (found in the HMIS reporting guidebook) Example: Flammable liquids, Corrosives, Cryogenics, etc.

4.  COMPLETE THE HMIS DOCUMENT: Remember: You are reporting the MAXIMUM AMOUNT OF THE CATEGORY THAT IS ON HAND DURING THE CALENDAR YEAR. Directions are found in the HMIS Reporting Guidebook.

5.  IF YOU’RE NOT SURE HOW TO CLASSIFY the chemical, review the definition found in the HMIS reporting guidebook for that chemical. If you still cannot determine how to classify the product, contact the manufacturer. Their info is on the MSDS.

6.  EXTREMELY HAZARDOUS SUBTANCES (EHS): You must report EHS’s. If you’re not sure if you have EHS’s, you can check the list at this web site: http://www.michigan.gov/documents/deq/deq-ead-sara-ehslist_305998_7.pdf

7.  ONCE COMPLETED, SAVE A COPY OF THE FILE: Save a copy of the HMIS

form for your files.

8.  SURVEY THE FACILITY: Create a floor plan that shows:

Locations where reportable quantities of hazardous materials are stored, used or manufactured.

Identify site specific features on a floor plan, including but not limited to: Natural Gas Shut Off Location	Fire Alarm Panel

Electric Utility Shut Off Location	Fire Doors & Fire Walls

Fire Suppression Control Valves	Exit Doors

9.  PROVIDE THE FIRE DEPARTMENT WITH AN ELECTRONIC FLOOR PLAN OF THE FACILITY: The floor plan should reflect how to get in and out, as well as the items mentioned above.  A sample floor plan has been attached to show you what we need on your drawings.  YOU MUST SEND US A FLOOR PLAN DRAWING REGARDLESS OF WHETHER  HAVING ANY HAZARDOUS MATERIALS OR NOT!

10. COMPLETE THE EMERGENCY CONTACT FORM: This form is located in the back of the “Hazardous Materials Reporting Handbook”. It is self-explanatory.  Please be thorough. This information is used in the event we must contact a facility representative after normal operating hours. Send it electronically.

11. PERMIT APPLICATION: A fire inspector will review your HMIS form and the supporting documentation and will determine what permit, if any, will be required.

THIS PAGE INTENTIONALLY LEFT BLANK

Evart Area Fire Department

109 East Sixth St., Evart, MI 49631

Business # 231 734 5521 Fax # 231 734 2476

"Protecting Your Future"

TO: Business Owner / Manager

RE: Hazardous Materials Reporting Requirements

To Whom It May Concern:

Section 14i of the Michigan Occupational Safety and Health Act (MI-OSHA), Act No. 154, P.A. of 1974, as amended, requires that each fire chief prepare and disseminate to each fire fighter information on facilities within their jurisdiction that use or produce hazardous chemicals.

The Michigan Fire Prevention Code, Act No. 207, P.A. of 1941, as amended, requires that any firm handling hazardous chemicals provide information to the fire chief upon request. This allows the fire department to gather information on each chemical so that the requirements of MI-OSHA can be met.

To assist our department in fulfilling its responsibilities under these requirements, we are requesting that you perform the following if you have quantities of hazardous chemicals equal to or greater than what is defined in the attachment:

	Complete the Hazardous Material Inventory Statement (HMIS) and return within 30 days. The form can be obtained on the internet at: evartfd.com.

	A fill-in-the-blank spreadsheet will also be available within this form.  It can be filled in and printed out.  You will be able to complete this form  in its entirety on line but will not be able to save it. You will be able to save a copy of this in MS Word. Directions are included in this packet.  Your choice on which form you use.

	Your completed forms are to be e-mailed to s.helmer@evartfd.com or faxed to the Fire Marshal at 231 734 2476.  In the “Subject” line of the e-mail, insert “HMIS PACKET RETURN – (Your Business Address)”.

	Complete the enclosed Emergency Contact Form. This information is critical if we need to contact you after hours. Please be complete with this information and it can only be faxed into our office.

	Provide    an    electronic    building    floor    plan.    Plan    is    to    be    e-mailed    to s.helmer@evartfd.com.  In the “Subject” line of the e-mail, insert “Haz-Mat Floor Plan – (Your Business Address)”.  A sample floor plan has been attached to show you what we need on your drawings.

	Do not return Material Safety Data Sheets (MSDS) at this time.

This information is beneficial to our fire fighters when responding to a fire or other emergency at your facility. If your firm does not use or produce any hazardous chemicals, you still must

Last Updated: February 2013

complete the form. Just fill in the general information requested on the top of the form. Emergency personnel hold all telephone numbers in strict confidence and are for emergency use only and will not give out to anyone.

If you have no reportable quantities of hazardous materials, check the box labeled “NO REPORTABLE QUANTITIES” at the top of the form.

If the information you provide indicates that your firm is a user, producer, or otherwise handles hazardous chemicals and the chemicals on site meet or exceed the specified quantities, we will be contacting you for further information. This may include specific locations of the chemicals at your facility; MSDS’s; or to schedule a fire inspection.

To complete the HMIS form, go to evartfd.com.  Take care to complete the HMIS form, and emergency contact form.  Also, include an electronic building floor plan. Then, return them via e-mail to:  s.helmer@evartfd.com.  This form must be completed and returned within thirty  days.  All  surveys,  including  negative  responses,  are  kept  on  file  for  a predetermined amount of time to satisfy state and local requirements.

If you cannot access our web page, current copies of these forms are available electronically. You can request the forms by sending an e-mail to  s.helmer@evartfd.com or you can stop by our office and ask to have an HMIS Packet be sent to you.  By using  this  form,  you  can  maintain  your  compliance  with  MI-OSHA  rules  and  save  the information electronically for easy retrieval.

If there is a change concerning the use, productions, or quantity of hazardous chemicals at your facility in the future, please contact this department so that we may direct you on how to update the files. Once again, any questions concerning this matter can be directed to the Fire Prevention Bureau at 231 734 5521 or MI-OSHA. Thank you in advance for your cooperation.

Protecting Your Future!

Shane Helmer, Fire Chief

Evart Area Fire Department

Last Updated: February 2013

INS T R UC T IONS	F O R 	C OM P L ETI N G T HE	HM I S		DOC UM E NT

Start in the upper left corner.  Fill in all requested information.

1. CHEMICAL NAME: This is the chemical name of the product, not the trade name. (Example: Report “Gasoline”, not “Shell Gas”, or “Mobil Gas”.)

2. TRADE NAME: This is the trade name of the product. (Example: Report

“Thompson’s Water Seal”, not “Silicone”).

HOW TO REPORT MIXTURES: Mixtures of chemicals shall not be reported as each individual chemical in the mixture. Rather, report mixtures as a single product.

3. FD HAZ CLASS: This is the Fire Department Hazard Classification Number.  It is the classification of the product as described in the section entitled: “Reportable Quantities”.  It defines the categories and helps to place chemicals in the proper hazard class number. The “Reportable Quantities” document identifies the Fire Department Hazard Class. The “Reportable Amounts Table” lists the “trigger amounts” for reporting that hazard class. (Example: You have 3 chemicals in FD Hazard Class “21”.  If the three chemicals together total less than 30 gallons, you do not have to report them. But if together they total 30 gallons or more, then you shall report them on this form.)

4. EHS: This stands for Extremely Hazardous Substance (EHS). If this is an EHS, it may be noted on the MSDS. To find a list of EHS’s, go to: http://www.michigan.gov/documents/deq/deq-ead-sara-ehslist_305998_7.pdf

5. D.O.T. UN/NA NUMBER: This is a four-digit number that quickly identifies the specific or generic hazards of the product for emergency responders and handlers during the initial response phase of an emergency involving that product. The number is provided on the Material Safety Data Sheet (MSDS) for the product you are reporting.  (Examples: 1017 – Chlorine, 1075 – LPG, 1744 – Bromine)

6. C.A.S. NUMBER: C.A.S. stands for Chemical Abstracts Service.  Key Point: CAS

numbers identify the chemical, but not its concentration or specific mixture.

7. NFPA 704 NUMBER: This is a nationally recognized standard adopted by the fire service that addresses the health, flammability, instability, and related hazards that are presented by short-term, acute exposure to a material under conditions of fire, spill, or similar emergencies.

The system identifies hazards in three basic categories. They are: Health (H), Flammability (F) and Instability (or Reactivity) (R). The hazard is graded on a scale of zero to four, with four being the most severe. This information can be found on the MSDS for the product.

8. REPORTABLE QUANTITIES - AMOUNT ON SITE: This is the total amount of product that will be stored, delivered, manufactured and or used on site during the calendar year.  In other words, what is the largest amount of product you will have at any one time.  Please list this amount in English measure and in the physical state (see next definition) that the product is in at normal temperature, time and pressure.

- Continued -

Last Revised: April 2011

INS T R UC T IONS	F O R 	C OM P L ETI N G T HE	HM I S		DOC UM E NT

9. PHYSICAL STATE OF MATERIALS: Examples: Solid, Liquid, Gas, Powder, Cryogenic, etc.)

10. LOCATION OF MATERIALS: This refers to the physical location of where the product is used, manufactured or stored at this site. Please indicate if the product is located inside or outside.  Also, provide a scale drawing of this site on 8.5” by 11” paper identifying the location(s), as well as an electronic version of the drawing in either “*.pdf” or “*.tiff” format.  Any questions on this, please call the Fire Marshal.

NOTE: The drawing should also include information such as: location of the fire alarm control panel (FACP), fire department connection (FDC), fire suppression system control valve room, Utility shut off locations, Fire Department Lock Box location and the location of the Inspector’s Test Valve (ITV) for the fire sprinkler system.

NO REPORTABLE QUANTITIES: If the total amount of product you have is less than the amount required to report, please indicate by checking the appropriate box on the top of the HMIS form.

Last Revised: April 2011

Reportable Quantities shall be considered the maximum amount of material on site at any given time that shall be reported to the fire department.  (Example: If a process uses one drum per month of material but that material is ordered at ten drums each time, then the maximum quantity would be the total amount contained in the ten drums.)  Reportable amounts are listed on the table found near the end of this document. NOTE: The definitions are filed alphabetically. The FD Hazard Class number precedes each definition.

Aerosol: A product that is dispensed from an aerosol container by a propellant.

Anhydrous Ammonia: A compound formed by a combination of two gaseous elements, nitrogen and hydrogen, in the proportion of one part nitrogen to three parts hydrogen by volume. Anhydrous ammonia may be in either gaseous or liquid form. It is not to be confused with aqueous ammonia, which is a solution of ammonia gas in water.

Carcinogens: A chemical that is capable of causing cancer as defined by the International Agency for Research on cancer is listed as a carcinogen or potential carcinogen in the Annual Report on Carcinogens published by the National Toxicology Program, or is regulated by OSHA as a carcinogen.

Combustible: Able to catch fire and burn regardless of its auto-ignition point or whether it is a solid, liquid or gas.

Combustible Liquids: A liquid having a closed cup flash point at or above 100O F (38OC). Combustible liquids shall be subdivided as follows:

Class II: Liquids having a closed cup flash point at or above 100O F (38O C) and below

140O F (60O C).

Class IIIA: Liquids having a closed cup flash point at or above 140O F (60O C) and below

200O F (93O C).

Class IIIB: Liquids having a closed cup flash point at or above 200O F (93O C).

Combustible Fibers: Readily ignitable and free burning fibers such as cotton, sisal, henequen, jute, hemp, tow, cocoa fiber, oakum, baled waste, baled wastepaper, kapok, hay, straw, excelsior, Spanish moss and other like material.

Compressed Gas: A material or mixture of materials which:

1. Is a gas at 68_F (20_C) or less at 14.7 psia (101 kPa) of pressure; and

2. Has a boiling point of 68_F (20_C) or less at 14.7 psia (101 kPa) which is either liquefied, non-liquefied or in solution, except those gases which have no other health- or physical-hazard properties are not considered to be compressed until the pressure in the packaging exceeds 41 psia (28 kPa) at 68_F (20_C).

The states of a compressed gas are categorized as follows:

1. Non-liquefied compressed gases are gases, other than those in solution, which are in a packaging under the charged pressure and are entirely gaseous at a temperature of

68_F (20_C).

– Continued –

Compressed Gas: The states of a compressed gas are categorized as follows: (Continued)

2. Liquefied compressed gases are gases that, in a packaging under the charged pressure, are partially liquid at a temperature of 68_F (20_C).

3. Compressed gases in solution are non-liquefied gases that are dissolved in a solvent.

4. Compressed gas mixtures consist of a mixture of two or more compressed gases contained in a packaging, the hazard properties of which are represented by the properties of the mixture as a whole.

Corrosive Gas: A gas that causes visible destruction of, or irreversible alterations in, living tissue by chemical action at the point of contact. A chemical shall be considered corrosive if, when tested on the intact skin of albino rabbits by the method described in DOT 49 CFR, Part 173, such chemical destroys or changes irreversibly the structure of the tissue at the point of contact following an exposure period of 4 hours. This term does not refer to action on inanimate surfaces.

Flammable Gas: A material which is a gas at 68°F (20°C) or less at 14.7 pounds per square inch atmosphere (psia) (101 kPa) of pressure [a material that has a boiling point of

68°F (20°C) or less at 14.7 psia (101 kPa)] which:

1. Is ignitable at 14.7 psia (101 kPa) when in a mixture of 13 percent or less by volume with air; or

2. Has a flammable range at 14.7 psia (101 kPa) with air of at least 12 percent,

regardless of the lower limit. The limits specified shall be determined at 14.7 psi (101 kPa) of pressure and a temperature of 68°F (20°C) in accordance with ASTM E 681.

Non-Flammable Gas: Any compressed gas other than a flammable compressed gas.

Corrosive Liquids: Those acids, alkaline caustic liquids, and other corrosive liquids which, when in contact with living tissue, will cause severe damage to such tissue by chemical action; or in case of leakage, will materially damage or destroy other containers of other hazardous commodities by chemical action and cause the release of their contents; or capable of causing fire when in contact with organic matter or certain chemicals.

Corrosive Solid: A solid material that causes visible destruction of, or irreversible alterations in, living tissue by chemical action at the point of contact. A chemical shall be considered corrosive if, when tested on the intact skin of albino rabbits by the method described in DOT 49 CFR, Part

173, such chemical destroys or changes irreversibly the structure of the tissue at the point of contact following an exposure period of 4 hours. This term does not refer to action on inanimate surfaces.

Cryogenic Fluid: Any liquid having a boiling point lower than –130O F (-89.9O C) at 14.7 pounds per square inch atmosphere (psia) (an absolute pressure of 101.3 kPa).

Cryogenic Liquid (Flammable): A cryogenic fluid that is flammable in its vapor state.

Cryogenic Oxidizer: A cryogenic agent that releases oxygen and will easily combine with fuels to burn. It is a liquid only at very low temperatures.

Explosive & Blasting Agent:

Explosive: A chemical compound, mixture or device, the primary or common purpose of which is to function by explosion. The term includes, but is not limited to, dynamite, black powder, pellet powder, initiating explosives, detonators, safety fuses, squibs, detonating cord, igniter cord, igniters and display fireworks, 1.3G (Class B, Special). The term “explosive” includes any material determined to be within the scope of USC Title 18: Chapter  40  and  also  includes  any  material  classified  as  an  explosive  other  than consumer fireworks, 1.4G (Class C, Common) by the hazardous materials regulations of DOT 49 CFR.

Blasting Agent: A material or mixture consisting of fuel and oxidizer, intended for blasting provided that the finished product, as mixed for use or shipment, cannot be detonated by means of a No. 8 test detonator when unconfined. Blasting agents are labeled and placarded as Class 1.5 material by US DOT.

Liquefied Natural Gas (LNG): A fluid in the liquid state composed predominantly of methane and which may contain minor quantities of ethane, propane, nitrogen or other components normally found in natural gas.

Liquefied Petroleum Gas (LPG): A material that is composed predominantly of the following hydrocarbons or mixtures of them: propane, propylene, butane (normal butane or isobutane) and butylenes.

Flammable  Liquid:  Any  liquid  having  a  closed  cup  flash  point  below  100O   F  (38O   C). Flammable liquids are further categorized into a group known as Class I Liquids.  The Class I category is subdivided as follows:

Class 1A: Liquids having a flash point below 73O  F (23O  C) and having a boiling point below 100O F (38O C).

Class 1B: Liquids having a flash point below 73O F (23O C) and having a boiling point at or above 100O F. (38O C).

Class 1C: Liquids having a flash point at or above 73O  F. (23O  C) and below 100O  F. (38O C).

Flammable Solid: A solid, except a blasting agent or explosive, capable of causing fire through friction, absorption of moisture, spontaneous chemical change, or retained heat from manufacturing or processing, or which has an ignition temperature below 212O  F (100O  C) or which burns so vigorously and persistently when ignited as to create a serious hazard.

Irritating Material: A chemical that is not corrosive, but causes a reversible inflammatory effect on living tissue by chemical action at the site of contact.

- Continued –

Irritating Material: (Continued)

(a) For the purpose of Code of Federal Regulations Parts 170 through 189 of this subchapter, an irritating material is a liquid or solid substance which upon contact with fire or when exposed to air gives off dangerous or intensely irritating fumes, such as bromobenzylcyanide, chloracetophenone, diphenylamine chlorarsine, and diphenyl chlorarsine, but not including any poisonous material, Class A.

Organic Peroxide: An organic compound that contains the bivalent -O-O- structure and which may be considered to be a structural derivative of hydrogen peroxide where one or both of the hydrogen atoms have been replaced by an organic radical. Organic peroxides can pose an explosion hazard (detonation or deflagration) or they can be shock sensitive. They can also decompose into various unstable compounds over an extended period of time.

Class I: Those formulations that are capable of deflagration but not detonation.

Class II: Those formulations that burn very rapidly and that pose a moderate reactivity hazard.

Class III: Those formulations that burn rapidly and that pose a moderate reactivity hazard.

Oxidizing Gas: A gas that can support and accelerate combustion of other materials.

Oxidizer: A material that readily yields oxygen or other oxidizing gas, or that readily reacts to promote or initiate combustion of combustible materials. Examples of other oxidizing gases include bromine, chlorine and fluorine.

Class 1: An oxidizer whose primary hazard is that it slightly increases the burning rate but which does not cause spontaneous ignition when it comes in contact with combustible materials.

Class 2: An oxidizer that will cause a moderate increase in the burning rate or that causes spontaneous ignition of combustible materials with which it comes in contact.

Class 3: An oxidizer that will cause a severe increase in the burning rate of combustible materials with which it comes in contact or that will undergo vigorous self-sustained decomposition due to contamination or exposure to heat.

Class   4:   An   oxidizer   that   can   undergo   an   explosive   reaction   due   to contamination or exposure to thermal or physical shock. In addition, the oxidizer will enhance the burning rate and can cause spontaneous ignition of combustibles.

Poison: Toxic liquid or solid substance that is a hazard to health.

Pyrophoric: A material that will spontaneously ignite in air at or below a temperature of 130OF.

Radioactive: Any material or combination of materials that spontaneously release ionizing radiation.

Spontaneously  Combustible  Material:  A  material  that  may  ignite  by  the  heat  produced through chemical action of its own components.

Toxic Material: A chemical falling within any of the following categories:

A chemical that has a median lethal dose (LD 50) of more than 50 milligrams per kilogram, but not more than 500 milligrams per kilogram of body weight when administered orally to albino rats weighing between 200 and 300 grams each, or,

A chemical that has a median lethal dose (LD 50) of more than 200 milligrams per kilogram but not more than 1,000 milligrams per kilogram of body weight when ad- ministered by continuous contact for 24 hours (or less if death occurs within 24 hours) with the bare skin of albino rabbits weighing between 2 and 3 kilograms each, or,

A chemical that has a median lethal concentration (LC 50) in air of more than 200 parts per million but not more than 2,000 parts per million by volume of gas or vapor, or more than 2 milligrams per liter but not more than 20 milligrams per liter of mist, fume or dust, when administered by continuous inhalation for 1 hour (or less if death occurs within 1 hour) to albino rats weighing between 200 and 300 grams each.

Highly Toxic Material: A material that produces a lethal dose or lethal concentration that falls within any of the following categories:

1.   A chemical that has a median lethal dose (LD 50) of 50 milligrams or less per kilogram of body weight when administered orally to albino rats weighing between 200 and 300 grams each.

2.	A chemical that has a median lethal dose (LD 50) of 200 milligrams or less per kilogram of body weight when administered by continuous contact for 24 hours (or less if death occurs within 24 hours) with the bare skin of albino rabbits weighing between 2 and 3 kilograms each.

3.   A chemical that has a median lethal concentration (LC 50) in air of 200 parts per million by volume or less of gas or vapor, or 2 milligrams per liter or less of mist, fume or dust, when administered by continuous inhalation for one hour (or less if death occurs within 1 hour) to albino rats weighing between 200 and 300 grams each.

Mixtures of these materials with ordinary materials, such as water, might not warrant classification as highly toxic. While this system is basically simple in application, experienced, technically competent persons shall perform any hazard evaluation that is required for the precise categorization of this type of material.

– Continued –

Unstable (Reactive) Material: Substances capable of rapidly undergoing chemical changes or decomposition. Materials that polymerize, decompose, condense or become self-reactive when exposed to air, water, heat, shock or pressure.

Class 2: Materials that readily undergo violent chemical change at elevated temperatures and pressures.

Class 3: Materials that, in themselves, are capable of detonation or explosive decomposition or explosive reaction, but that require a strong initiating source or that must be heated under confinement before initiation.

Class 4: Materials, that in themselves are, readily capable of detonation or explosive decomposition or explosive reaction at normal temperatures and pressures.

Water Reactive Material: A chemical that reacts with water to release a gas that is either flammable or presents a health hazard.

Class 2: Materials that are capable of forming potentially explosive mixtures with water.

Class 3: Materials that react explosively with water without requiring heat or confinement.

| REPORTABLE QUANTITIES OF HAZARDOUS MATERIALS (Quantities equal to or greater than listed) |
| --- |
| FD HAZ CLASS | MATERIAL | HOW or WHERE MATERIAL IS STORED OR USED | REPORTABLE AMOUNT |
| 1 | AEROSOLS: LEVEL 2 OR 3 |  | 500 LBS. |
| 2 | ANHYDROUS AMMONIA (Corrosive Gas) |  | 200 Cu. Ft. |
| 3 | CARCINOGENS |  | Any Amount |
| 4 | COMBINATION FLAMMABLE LIQUIDS | Inside | 5 Gallons |
|  |  | Outside | 10 Gallons |
|  | COMBUSTIBLE LIQUIDS |  |
| 5 | CLASS II | Inside / Outside | 25 Gal. / 60 Gal. |
| 5A | CLASS III-A | Inside / Outside | 25 Gal. / 60 Gal. |
| 5B | CLASS III-B |  | 3,300 Gallons |
| 6A | COMBUSTIBLE FIBER (Loose) | Loose | 20 cu.ft. |
| 6B | COMBUSTIBLE FIBER (Baled) | Baled | 100 cu.ft. |
|  | COMPRESSED GASES |  |
| 7A | CORROSIVE |  | 200 cu.ft |
| 7B | FLAMMABLE (Except: Cryogenic Fluids & Liquid Petroleum Gases |  | 200 cu.ft |
| 7C | HIGHLY TOXIC |  | Any Amount |
| 7D | INERT & SIMPLE ASPHYXIANT |  | 6,000 cu.ft. |
| 7E | OXIDIZING (Including Oxygen) | Liquefied / Gaseous | 504 cu.ft. |
| 7F | TOXIC |  | Any Amount |
| 7G | NON-FLAMMABLE GAS |  | 100 Gals. Water Cap. |
| 8A | CORROSIVE LIQUIDS |  | 55 Gallons |
| 8B | CORROSIVE SOLIDS |  | 500 LBS. |
|  | CRYOGENIC FLUIDS |  |
| TYPE OF CRYOGENIC FLUID |  |
| 9A | Flammable | Inside / Outside | > 1 Gal. / 60 Gals. |
| 9B | Inert | Inside / Outside | 60 Gals / 500 Gals. |
| 9C | OXIDIZING (Including Oxygen) | Inside / Outside | 10 Gals. / 50 Gals. |
| 9D | Physical or health hazard not indicated above | Inside / Outside | Any Amount |
| 10 | EXPLOSIVE & BLASTING AGENTS: (Not including Class "C" explosive) |  | Any Amount |
| 11 | LIQUEFIED NATURAL GAS |  | 5 Gallons |
| 12 | LIQUEFIED PETROLEUM GAS |  | 5 Gallons |

R EP O R TA B LE	A M O U N TS	T A B LE

(EFFECTIVE: JANUARY 2010)

REPORTABLE QUANTITIES OF HAZARDOUS MATERIALS (Quantities equal to or greater than listed)

FD	HOW or WHERE

HAZ CLASS

MATERIAL

FLAMMABLE LIQUIDS

MATERIAL IS STORED OR USED

REPORTABLE

AMOUNT

13A	CLASS 1-A	5 GALLONS

13B	CLASS 1-B	5 GALLONS

13C	CLASS 1-C	5 GALLONS

14	Flammable Solid	25 lbs

15L	IRRITATING MATERIAL (Liquid)	1,000 GAL.

15S	IRRITATING MATERIAL (Solid)	500 LBS.

ORGANIC PEROXIDES

16L-1	CLASS I

Any Amount

16L-2	CLASS II	Any Amount

Liquid

16L-3	CLASS III	1 Gallon

16L-4	CLASS IV	2 Gallons

16S-1	CLASS I

Any Amount

16S-2	CLASS II	Any Amount

Solid

16S-3	CLASS III	10 lbs.

16S-4	CLASS IV	20 lbs.

OXIDIZERS

7E	OXIDIZING GAS	504 CU. FT. @ NTP

17L-4	CLASS 4

Any Amount

17L-3	CLASS 3	1 Gallon

Liquid

17L-2	CLASS 2	10 Gallons

17L-1	CLASS 1	50 Gallons

17S-4	CLASS 4

Any Amount

17S-3	CLASS 3	10 lbs.

Solid

17S-2	CLASS 2	100 lbs.

17S-1	CLASS 1	500 lbs.

18L

Poison

Liquid	50 Gals.

18S	Solid	500 lbs.

19G

19L

Pyrophoric

Gases	10 cu.ft. @ NTP Liquid	Any Amount

19S	Solid	Any Amount

20	Radioactive Material	Any Amount

21	SPONTANEOUSLY COMBUSTIBLE MATERIAL	100 LBS.

| REPORTABLE QUANTITIES OF HAZARDOUS MATERIALS (Quantities equal to or greater than listed) |
| --- |
| FD HAZ CLASS | MATERIAL | HOW or WHERE MATERIAL IS STORED OR USED | REPORTABLE AMOUNT |
|  | TOXIC MATERIAL |  |
| 22S | Toxic Material | SOLID | 100 lbs. |
| 22L |  | LIQUID | 10 Gals. |
| 22G |  | GAS | Any Amount |
|  | HIGHLY TOXIC MATERIAL |  |
| 23S | Toxic Material (Highly) | SOLID | 10 lbs. |
| 23L |  | LIQUID | 10 Gals. |
| 23G |  | GAS | Any Amount |
|  | UNSTABLE (REACTIVE) MATERIAL |  |
| 24L-1 | CLASS 1 | Liquid | 10 Gals. |
| 24L-2 | CLASS 2 |  | 5 Gals. |
| 24L-3 | CLASS 3 |  | Any Amount |
| 24L-4 | CLASS 4 |  | Any Amount |
| 24S-1 | CLASS 1 | Solid | 100 LBS. |
| 24S-2 | CLASS 2 |  | 50 LBS. |
| 24S-3 | CLASS 3 |  | Any Amount |
| 24S-4 | CLASS 4 |  | Any Amount |
|  | WATER REACTIVE MATERIAL |  |
| 25L-1 | CLASS 1 | Liquid | 55 Gals |
| 25L-2 | CLASS 2 |  | 5 Gals |
| 25L-3 | CLASS 3 |  | Any Amount |
| 25S-1 | CLASS 1 | Solid | 500 Lbs |
| 25S-2 | CLASS 2 |  | 50 Lbs |
| 25S-3 | CLASS 3 |  | Any Amount |

EMERGENCY CONTACT FORM

I n f o r m a t i on c ont a i n e d on t hi s f or m i s f or O f f i c i a l U s e O nl y a n d  i s  N O T  F O R  P U B LI C  EY ES

DIRECTIONS:

This information is being requested to update our files.  Please “…provide a current list of emergency contacts who will respond to the premises in the event of an emergency, or to reset or deactivate the alarm system, or who could contact the alarm user if the alarm user is not at the scene.”  In the event of an emergency at your location, the fire department would be able to access this information and make timely contact with you or one of your employees.

When filling out this form, please do the following:

•	Make a copy of the blank form.  Then set the original aside.

•	Fill out the blank copy with the information requested.  Please list key holders that will respond if required by the Fire Department in case of emergency.	The more information provided, the sooner the fire department can contact you in the event of an emergency.

•	Fax the form, to our office at 231 734 5521, or Email it to: s.helmer@evartfd.com.  (If you cannot fax or email it, make a copy of the completed form.  Place one completed copy in an envelope and mail it to our office).

•	After you have provided a copy to this office, take the completed copy and the blank original and file it away until next year.  At that time, review the information for any changes.  If any changes have been made, make a copy of the blank form, fill in the changes and e-mail or fax it to our office.

•	If you have a Lock Box and change keys, you must contact our office.

•	If you have any questions, please contact the fire department office.

EMERGENCY CONTACT FORM

I n f o r m a t i on c ont a i n e d on t hi s f or m i s f or O f f i c i a l U s e O nl y a n d  i s  N O T  F O R  P U B LI C  EY ES

BUSINESS NAME:

BUSINESS ADDRESS:

PRIMARY EMERGENCY CONTACT PERSON (During & AFTER Hours):

NAME:  				  TITLE:  				 HM ADDRESS:  				  HM PHN:  		 WK PHN:  	 CELL:  	 OTHER:

SECONDARY EMERGENCY CONTACT PERSON (During & AFTER Hours):

NAME:  				  TITLE:  				 HM ADDRESS:  				  HM PHN:  		 WK PHN:  	 CELL:  	 OTHER:

CONTINGENT EMERGENCY CONTACT PERSON (During & AFTER Hours):

NAME:  				  TITLE:  				 HM ADDRESS:  				  HM PHN:  		 WK PHN:  	 CELL:  	 OTHER:

CHECK ALL THAT APPLY:

Have Lock Box	Have Monitored Fire Alarm	Have Monitored Fire Suppression

(Add additional sheets if you would like to add additional people to this list.)

DATE INFO

ENTERED:	Jan. 8, 2009	INFO EXPIRES:	Jan. 8, 2012

INFO ENTERED BY / CONTACT PERSON:

CONTACT PERSON E-MAIL ADDRESS:

REPORT INFORMATION

EXPIRES:	3	YEARS AFTER SUBMITTAL

DAYTIME CONTACT PHONE:

P.F. #:

FACILITY NAME:	FACILITY ADDRESS: FACILITY

PHONE:	FACILITY FAX:

If you have No Reportable

HMIS Document

Version:	January 2010

Quantities, place an "X" in this box:

INFORMATION CONTAINED IN THE SHADED AREAS ARE FOR EXAMPLES ONLY. IT DOES NOT REPRESENT ANY PRODUCT THAT IS, OR MAY BE, ON-SITE AT THIS LOCATION.

NFPA

704 (No.

1-4)

REPORTABLE QUANTITIES AMOUNT ON SITE

PHYSICAL STATE OF

MATERIAL	LOCATION

INSIDE / OUTSIDE /

CHEMICAL

NAME	TRADE NAME

FD HAZ CLASS.

DOT

UN/NA No.

C.A.S.

NO.	H	F	R	GALS	LBS

CU. FT

BOTH (IDENTIFY LOCATIONS ON SITE DRAWING)

Ethyl Alcohol	Ethanol	15		1170	64-17-5	0	3	0	500	x	(I) Room A Hydrogen Cyanide	Hydrogen Cyanide	36	X	1051	 74908	4	4	2	 30	x	(O) Shed

Last Revised: April 2011

Evart Area  FIRE DEPARTMENT HAZARDOUS MATERIALS INVENTORY STATEMENT

| DATE INFO ENTERED: |  | INFO EXPIRES: |  | REPORT INFORMATION EXPIRES: 3 YEARS AFTER SUBMITTAL |
| --- | --- | --- | --- | --- |
| INFO ENTERED BY / CONTACT PERSON: |  | DAYTIME CONTACT PHONE: |  |  |
| CONTACT PERSON E-MAIL ADDRESS: |  | P.F. #: |
| FACILITY NAME: |  | FACILITY ADDRESS: |  |
| FACILITY PHONE: |  | FACILITY FAX: |  |
| HMIS Document Version: May 2009 | If you have No Reportable Quantities , place an "X" in this box: |  |  |
| INFORMATION CONTAINED IN THE SHADED AREAS IS FOR EXAMPLE ONLY. IT DOES NOT REPRESENT ANY PRODUCT THAT IS, OR MAY BE, ON-SITE AT THIS LOCATION. | NFPA 704 (No. 1-4) | REPORTABLE QUANTITIES AMOUNT ON SITE | PHYSICAL STATE OF MATERIAL | LOCATION |
| CHEMICAL NAME | TRADE NAME | FD HAZ CLASS. | E H S | DOT UN/NA No. | C.A.S. NO. | H | F | R | GALS | LBS | CU. FT | L I Q | S O L | G A S | G R A N | P W D R | C R Y O | INSIDE / OUTSIDE / BOTH (IDENTIFY LOCATIONS ON SITE DRAWING) |
| Ethyl Alcohol | Ethynol | 15 |  | 1170 | 64-17-5 | 0 | 3 | 0 | 500 |  |  | x |  |  |  |  |  | (I) Room A |
| Hydrogen Cyanide | Hydrogen Cyanide | 36 | X | 1051 | 74908 | 4 | 4 | 2 | 30 |  |  | x |  |  |  |  |  | (O) Shed |

Revised: April 2011	Page 1	Printed: 12/9/2010

Evart Area FIRE DEPARTMENT HAZARDOUS MATERIALS INVENTORY STATEMENT

REPORTABLE QUANTITIES AMOUNT ON SITE

PHYSICAL STATE OF

MATERIAL	LOCATION

Revised: September 2009	Page 2	Printed: 12/9/2010

# Text boxes

CRYO

PWDR

GRAN

GAS

SOL

LIQ

EHS

| INFORMATION CONTAINED IN THE SHADED AREAS IS FOR EXAMPLE ONLY. IT DOES NOT REPRESENT ANY PRODUCT THAT IS, OR MAY BE, ON-SITE AT THIS LOCATION. | NFPA 704 (No. 1-4) |  |  |  |  |  |  |  |  |  |  |
| --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- | --- |
| CHEMICAL NAME | TRADE NAME | FD HAZ CLASS. | E H S | DOT UN/NA No. | C.A.S. NO. | H | F | R | GALS | LBS | CU. FT | L I Q | S O L | G A S | G R A N | P W D R | C R Y O | INSIDE / OUTSIDE / BOTH (IDENTIFY LOCATIONS ON SITE DRAWING) |